## Slide 1
Teaching the robotics club
A practical workshop for high school mentors
MechaRAMS · Proposed workshop time: 120 minutes
Notes: 0–10 minutes: discuss why the YMCA program exists and what a beginner should experience. The educator keeps responsibility for supervision and local procedures. Ask each mentor to name a time someone helped them learn without taking over.

## Slide 2
The robot setup
A Left wheel motor B Right wheel motor
C Forward distance sensor
D Downward color sensor
The auxiliary attachment motor stays unplugged.
Notes: 10–30 minutes: assemble and inspect the official base, trace physical cables, and run 00_mentor_smoke_test.py with wheels raised, then in a clear lane. This curriculum port map overrides the original build wiring. Label the robot front. Demonstrate the actual app and hub stop controls. Build PDF: https://assets.education.lego.com/v3/assets/blt293eea581807678a/blt06873e1b438a0d7e/5ec8e66f033ad5045f4c79a6/driving-base-bi-pdf-book1of1.pdf?locale=en-us

## Slide 3
A recipe inside a complete program
travel = 180
await drive(travel)
await signal("D")
Students edit the recipe. Mentors prepare the support code.
Notes: 30–50 minutes: mentors practice weeks 1–3. The recipe function in the actual file is called student_recipe. Explain wheel degrees, variables, and counted loops. Have every mentor predict before running. Use current SPIKE App 3 modules, not Legacy or Pybricks examples. App help: https://spike.legoeducation.com/prime/modal/help/lls-help-python

## Slide 4
Sensor decisions
A valid gap of 150 mm or less means parking is close.
A negative distance reading means check the sensor.
A dark marker needs a measured reflection threshold.
A movement limit means the target was not detected.
Notes: 50–70 minutes: use 00_sensor_readings.py while stationary. Compare readings with a ruler and with bright/dark surfaces. Run bounded movement only after the readings make sense. Source for distance units and invalid reading check: https://education.lego.com/en-au/lessons/spike-python-u3-sensor-control/spike-python-u3l3/. The helper code also checks after the final permitted movement.

## Slide 5
A small attachment and a fair comparison
Sketch a plow that guides a lightweight cube.
Keep wheels and the color sensor clear.
Test two designs with the same program and start.
Store each pair’s removable attachment separately.
Notes: 70–85 minutes: build a flat bumper or U-shaped guide using spare pieces from the base kit. Geometry depends on the actual pieces, so the educator must prepare and photograph a working mount. The comparison should change one feature. Preserve both pairs’ components.

## Slide 6
The coaching conversation
What did you expect?
What did you observe?
What one change could test your idea?
Notes: 85–100 minutes: each mentor teaches a five-minute mini lesson to another mentor. Ask a question, give a little thinking time, offer one hint, and return control. Check that the mentor invites both students to explain. Avoid correcting the whole project while students watch.

## Slide 7
Two pairs share each robot
15–27 minutes First pair tests, second pair plans.
27–39 minutes Pairs switch stations.
39–49 minutes Each pair gets a five-minute retest.
Drivers swap midway through every robot turn.
Notes: 100–110 minutes: rehearse transitions and a keyboard-takeover scenario. With two laptops, devices stay at kit stations and planning uses paper. A pair gets about 17 minutes of direct robot time; each child gets a share of those minutes. Week 8 uses a different showcase schedule.

## Slide 8
Ready to lead a pod
Connect, stop, and restore a known-good project.
Explain this week’s idea and its common mistakes.
Give both students meaningful operating turns.
Save the pair’s work and record what actually happened.
Notes: 110–120 minutes: complete the mentor readiness check. Review YMCA procedures and who to ask for help. Evidence records use student IDs. Take photos or quotes only through the agreed permissions. The instructor guide includes a hardware acceptance record that must be completed on both kits.