## Slide 1
Parking assistant
A distance reading changes a decision
Week 4 · MechaRAMS at the YMCA
Notes: 0–5 minutes: welcome and retrieval. How can a robot decide when it is close enough without someone shouting stop?
Learning goal: Each student predicts a threshold decision and distinguishes a valid distance reading from an invalid reading.
Minimum success: The robot approaches a broad cardboard wall in small steps and stops around 150 mm away. The pair explains the threshold, invalid-reading stop, and movement limit.

## Slide 2
Today’s robot challenge
A broad cardboard wall
A measured distance threshold
A record of why the robot stopped
Notes: 5–10 minutes, or 7–12 in week 8. Show a live distance reading while the robot stays still. Python readings use millimeters. Trace the condition 0 <= gap <= stop_mm. An invalid negative value must stop the activity for a check.
Preparation: Mount the distance sensor before class. Open W04_parking.py. At 100, 150, and 250 mm, check readings against the ruler. Start about 300 mm from a broad, upright wall. Keep hands out of the lane.
The core challenge uses an assembled base and the supplied complete project.

## Slide 3
Sensor input and if conditions
stop_mm = 150
gap = distance_sensor.distance(port.C)
if 0 <= gap <= stop_mm:
await signal("P")
Reading fragment from a complete supplied Python project
Notes: This is a discussion fragment. It belongs in the supplied project, not in an empty file. The student function is named student_recipe. Show a live distance reading while the robot stays still. Python readings use millimeters. Trace the condition 0 <= gap <= stop_mm. An invalid negative value must stop the activity for a check.
Expected reasoning: 220 continues. 150 and 90 are near. -1 is invalid and must not be treated as a real near distance. At 170 with a threshold of 150, continue if a step remains.
Technical references: https://spike.legoeducation.com/prime/modal/help/lls-help-python ; https://tuftsceeo.github.io/SPIKEPythonDocs/SPIKE3.html

## Slide 4
A prediction before the run
Threshold: 150 mm. What happens at 220, 150, and 90?
How should the program handle -1?
Both partners explain a prediction before anyone presses Run.
Notes: 10–15 minutes in the standard lesson. At a 150 mm threshold, classify 220, 150, 90, and -1. Which readings mean near? Which means check the sensor?
Do not reveal the answer immediately. Ask students to point to a line or a measured value. Expected reasoning: 220 continues. 150 and 90 are near. -1 is invalid and must not be treated as a real near distance. At 170 with a threshold of 150, continue if a step remains.
Support: Provide the decision rule in words and highlight the threshold number. A stationary sensor demonstration can meet the decision objective if movement fails.

## Slide 5
Your work with a partner
Driver: edit and start after the lane check.
Navigator: predict, check, and record.
Swap roles halfway through your robot turn.
Away from the robot: complete the worksheet task.
Notes: Robot and planning rotations. 1. With wheels still, measure the wall distance using a ruler. Compare two sensor readings with the measured gap. Explain millimeters versus centimeters.
2. Set stop_mm = 150. Start roughly 300 mm away and run. The supplied helper checks the sensor before each short 30-wheel-degree movement and limits the run to 12 steps.
3. Measure the stopped distance and record the reason printed by the program: near, invalid, or limit. A limit message does not mean successful parking.
4. Swap roles. Try a 200 mm threshold from the same start. Predict whether the robot will stop sooner or later. Keep the wall broad and square to the sensor.
5. On the final turn, repeat one chosen setting. Explain why this classroom prototype is not a real vehicle safety system.
Off-robot task: Sort reading cards into continue, park, or sensor check. Plan expected behavior for a wall placed too far away. Use a ruler to convert 15 cm to 150 mm.
Week 8 schedule: 12–24 rehearsals, 24–28 setup, 28–44 demos. Otherwise 15–27 first pair, 27–39 second pair.

## Slide 6
Evidence from our test
We changed ____________________.
We predicted ____________________.
We observed ____________________.
Our next test would ____________________.
Notes: 39–49 minutes for improvement in standard lessons. Log threshold, start gap, stopped gap, and stop reason for two trials. Individual exit uses a new reading of 170 mm with a 150 mm threshold.
Troubleshooting: Invalid reading: check the C port and wall angle. Reaches step limit: move start closer or inspect readings. Stops too close: slow down and inspect step size. No collision is required to test the sensor.
Optional extension: Change one wall property, such as angle, and compare valid readings. Explain why poor readings require a fallback. Do not remove the step limit.
If Python becomes a barrier, preserve the concept using this fallback: Set near false. Repeat up to 12 checks: if distance is within a valid near range, set near true; otherwise, if still allowed, move straight a small increment. Use app distance units shown on the block, commonly cm: 15 cm equals 150 mm. Mentor verifies invalid-reading behavior and uses manual stop if needed.

## Slide 7
What you can explain now
What does the sensor supply, and what does the program decide?
Save your project. Reset the robot and parts for the next pair.
Sensors let an autonomous robot react to its surroundings.
Notes: 49–54 minutes: individual explanation. Reserve 54–60 for saving and reset. 220 continues. 150 and 90 are near. -1 is invalid and must not be treated as a real near distance. At 170 with a threshold of 150, continue if a step remains.
Sensors let an autonomous robot react to its surroundings.
Keep invitations to future activities optional and parent-mediated. Do not equate club attendance with FRC membership.